## Structure and Function of the Processor
- Often described as “the brain” of the computer. Misnomer: they don’t think they carry out instructions they are given.
- Made up of billions of transistors, which are essentially AND gates. Can be combined to form logic gates which in turn can be used to build the circuitry inside the CPU.
- Moore’s Law: Number of transistors on a processor would double approximately every two years. We are beginning to reach the limit of this.
- Processor speed is measured in Hertz which is the speed of the clock that the fetch decode execute runs to in cycles per second.
- Processors work by continually fetching instructions from memory, decoding them and executing them. The Fetch-Decode-Execute cycle.

Inside the Processor
Registers
- Memory locations within the processor itself. Work at fast speeds so can be used without causing a bottleneck.
- Program Counter (PC): Holds memory address of next instruction. Usually incremented by one each cycle however jump instructions can be used to alter the value in the PC and thus change the next instruction being fetched.
- Memory Data Register (MDR): The memory data register stores the data that has been fetched or is being stored to memory. Acts as a buffer for data or instructions.
- Memory Address Register (MAR): The memory address register stores the address of the data or instructions that are to be fetched or saved to.
- Current Instruction Register (CIR): The Current Instruction Register stores the most recently fetched instruction, waiting to be decoded and executed.
- The Accumulator (ACC): The accumulator stores the results of calculations made by the ALU.
- General Purpose Registers: Processors can gave these to stop data being constantly sent back and forth between memory and the CPU which is much slower.

Buses: Communications channel through which data can be sent around a computer. One example is USB (Universal Serial Bus) which transfers data between a computer and peripherals. There is also the address bus, data bus and memory bus.
Arithmetic Logic Unit (CLU): Carries out calculations and logical decisions the results of which are stored in the accumulator.
Control Unit (CU): Sends out signals to coordinate how the processor works. Controls how data and instructions are moved between memory and the CPU and around the CPU. Also decodes instructions.

Fetch-Decode-Execute Cycle
Fetch:
1. Program Counter copies the address of the next instruction into the Memory Address Register (MAR).
2. Memory Address Register places the address to be used on the address bus.
3. Control bus is used to send a read signal and the memory places the instruction being asked for on the data bus.
4. The instruction on the data bus is loaded into the MDR.
5. If it’s an instruction the MDR copies the instruction into the Current Instruction Register.

Decode:
1. CPU examines instruction in CIR and ‘decodes’ it. A special part of the CPU called the decode unit will make the rest of the CPU ready to carry out instruction. Every CPU has an instruction set that defines what the decoder understands as legitimate commands.

Execute:
1) The instruction within the CIR is carried out – executed – by the CPU. The part that does this is called the execute unit.
2) Reset – Now that the CPU is carrying out an instruction the PC can now be reset to point to the next instruction.